## Slide 1: MOTOR ASSEMBLY MONITORING THROUGH IMAGE ANALYSIS PROJECT ID-IN02
Team Members-
1)Arpan Kumar
4th year ECE
Academy of technology
2) Ayush Kumar
4th year EEE
Academy of technology
Team Mentor- Mr. Anik Sardar
Manager :Sensor QC & Calibration
Prophecy Sensorlytics India PVT.LTD.

## Slide 2: Problem Statement
The project focuses on developing an image analysis system to monitor the correct insertion of magnets into the rotor slots of a motor during assembly. Additionally, it includes a 3D surface scanning component to evaluate the surface roughness and depth variability of the motor post-assembly. The goal is to leverage advanced computer vision techniques to automate quality control processes, thereby reducing the reliance on manual inspections and enhancing overall production efficiency.

## Slide 3: Work Approach
Data Collection and Preprocessing:
  Gather stereo and RGB images of motor assemblies, including both properly placed and misaligned magnets.
  Convert RGB images to grayscale and preprocess them for noise reduction.
Image Comparison Algorithms:
  Develop algorithms using Structural Similarity Index (SSIM) to compare test images against reference images.
  Implement pixel-wise difference calculations to quantify deviations.
Depth Analysis Using Stereo Images:
  Generate disparity maps from stereo images to analyse depth discrepancies.
  Utilize depth analysis techniques to detect improperly inserted magnets.

## Slide 4
4. 3D Surface Scanning and Roughness Analysis:
  Extract 3D data from stereo images to create a point cloud representation of the motor surface.
  Analyse surface roughness and depth variability using statistical methods.
5. Decision-Making System Development:
  Create a threshold-based system to automatically flag assembly or surface quality issues based on analysis metrics.
  Analysed SSIM scores, insertion percentages, and surface roughness to make decisions on assembly quality.
6. Reporting and Visualization:
  Generated reports using matplotlib with visualizations to display the results.
  Created quality control reports indicating any assembly or surface issues detected.

## Slide 5: Work products and deliverables
Software Programs: Python scripts implementing image analysis, feature matching, depth analysis, and 3D surface scanning.
Datasets: Collection of stereo and RGB images showing different magnet alignment conditions.
Input folder name of images-new_images
reference image name-magnet_insertion-proper.jpg
GitHub Repository: A repository containing all source code, datasets, and documentations are present in this link: https://github.com/arpankumar2520/IDEAS_TIH_Project/tree/my-new-branch

## Slide 6: User Manual
Installation Requirements:
  Ensure Python is installed on your system.
  Install Jupyter Notebook.
  Install necessary libraries using the command:
pip install opencv-python scikit-image matplotlib.
2. Running the Application:
Execution:
  Run the main() function in the provided script.
  Specify the path for the reference image is “magnet_insertion-proper.jpg” and the folder with “new_images” which is containing the test images.
Output:
  View the results, including SSIM scores, surface roughness values, and insertion percentages.
  Check the automatically generated reports indicating quality control issues.

## Slide 7: Technical Manual
Datasets:
Captured Images: Stereo and RGB images of motor assemblies for analysis.
Software Libraries Used:
OpenCV: For Image processing and feature matching.
scikit-image: For SSIM calculation and surface roughness analysis.
Matplotlib: For Visualization of SSIM score distributions and analysis results.

## Slide 8: Program Documentation:
Load and preprocess images: Loads images, resizes the test image to the reference image’s.
Start
Load Reference and Test image
Check if Images Load Successfully
Show Error Message
Return Processed images
Convert to Grayscale
Resize Test image
End
YES
NO
The function first loads the reference and test images using `cv2.imread`. If the loading process fails, it displays an error message and terminates. Upon successful loading, the test image is resized to match the dimensions of the reference image using `cv2.resize`. Both images are then converted to grayscale using `cv2.cvtColor`. Finally, the function returns the original reference image, the resized test image, and their grayscale versions, as shown here.

## Slide 9
Comparing images: Calculates SSIM between reference and test images.
Start
End
Calculate SSIM
Calculate Absolute Difference
Normalize Difference Image
Return Difference image and Similarity Index
We compute the similarity index (SSIM) between the reference and test grayscale images to assess structural similarity. The SSIM score, ranging from -1 to 1, measures how closely the two images align, with a score of 1 indicating identical structures. High SSIM values suggest proper alignment, while lower values indicate potential alignment issues. For example, the SSIM for a fully inserted magnet is 1.0000, whereas the test images show an SSIM of approximately 0.8689, indicating alignment problems. Additionally, we calculate the absolute pixel-wise difference using `cv2.absdiff` and normalize this difference to a 0-255 range using `cv2.normalize`. The normalized difference image highlights mismatches and reveals misalignments or defects that SSIM alone may not capture. In this case, all images show magnet misalignment.
Fig: Displaying SSIM

## Slide 10
Determining the ssim threshold: Determines the SSIM threshold for classifying assembly accuracy.
Start
End
Calculate Mean SSIM
Return Threshold
Calculate Threshold (Mean + Standard Deviation)
Calculate Standard Deviation of SSIM
We compute the mean and standard deviation of the SSIM scores using `np.mean` and `np.std`, then calculate the threshold by adding the mean and standard deviation, returning the resulting threshold.
The reason for using the mean + standard deviation is that it provides a reliable, adaptive similarity level, avoiding overly strict or lenient arbitrary thresholds. This approach improves classification accuracy in quality control by accommodating acceptable variations. The mean plus standard deviation is chosen because it closely aligns with the SSIM values, unlike higher thresholds, which tend to differ significantly.
Fig: Comparing different
SSIM thresholding

## Slide 11
Analysing surface and Depth : Calculates surface roughness using standard deviation of the depth map. Generates disparity map for depth analysis.
Start
End
Calculate Disparity Map
Return Surface Roughness
Calculate Surface Roughness
Return Disparity Map
Surface Roughness values of all images
17.8853
20.1010
21.0387
17.6178
18.5573
18.5188
15.4731
35.9147
36.4679
We calculate the disparity map by finding the absolute pixel-wise difference between the reference and test grayscale images using `cv2.absdiff` and return the result. Surface roughness is then computed by calculating the standard deviation of the disparity map, which quantifies the variation in pixel values and provides insight into texture consistency. This analysis helps in detecting defects, ensuring quality, and supporting smooth operation in assembled parts. In this case, the approximated surface roughness is 22.3971, which is used to assess whether the magnet is properly inserted.

## Slide 12
Feature matching: Matches features between the reference and test images using ORB.
Start
End
Initialize ORB Detector
Detect Key points and Compute Descriptors (Reference Image)
Return Matches and Key points
Sort Matches by Distance
Match Descriptors
Create BF Matcher
Detect Key points and Compute Descriptors (Test Image)
We create an ORB (Oriented FAST and Rotated BRIEF) detector algorithm using `cv2.ORB_create()` to detect key points and compute descriptors for both the reference and test grayscale images. A brute-force matcher (`cv2.BFMatcher`) with Hamming distance is used to match the descriptors, and the matches are sorted by similarity. This feature matching process helps assess image similarity, aiding in quality control by identifying misaligned or missing components. The output includes the sorted matches and key points from both images, highlighting areas of similarity.
Fig: Feature matching

## Slide 13
Magnet insertion percentage and alignment score
Start
End
Define Threshold for Magnet Detection
Return Alignment Score
Calculate Alignment Score
Return Insertion Percentage
Calculate Insertion Percentage
Calculate Total Pixels
Calculate Inserted Pixels
We set a threshold value of 130 to identify pixels corresponding to inserted magnets. By counting the number of pixels below this threshold, we can determine magnet insertion. The total number of pixels in the test grayscale image is calculated, and the percentage of inserted pixels is computed by dividing the inserted pixel count by the total pixel count and multiplying by 100. This function returns the calculated magnet insertion percentage, which helps verify proper magnet insertion in the assembly and informs decision-making.
Additionally, the alignment score is calculated using the Structural Similarity Index (SSIM), which reflects how closely the test image matches the reference in terms of structure, texture, and other characteristics.
Fig: Values of magnet insertion and alignment score.

## Slide 14
Decision making: Quality control issues based on thresholds for SSIM, insertion, and roughness.
Start
End
Define Threshold
Decision: Surface Quality Issue
Decision: Partial Insertion (Insertion only)
Decision: Partial Insertion & Low SSIM
Decision: Partial Insertion (Low SSIM only)
Is SSIM below Threshold?
Is Insertion Percentage below Threshold?
Is Surface Roughness Exceed Threshold?
Is Insertion Percentage below Threshold?
Decision: Acceptable Assembly
NO
YES
NO
YES
NO
YES
NO
YES
We define thresholds for SSIM, insertion percentage, and surface roughness to assess the assembly quality. If the SSIM is below its threshold, we check whether the insertion percentage is also below its threshold. If both are low, we return a decision indicating partial insertion with low SSIM. If only SSIM is low, we return a decision indicating low SSIM with partial insertion. If the insertion percentage is below its threshold, we return a decision indicating partial insertion. Additionally, we check if the surface roughness exceeds its threshold; if it does, we return a decision indicating surface quality issues. If none of these conditions are met, we conclude that the assembly is acceptable.

## Slide 15
GitHub Repository Structure
Reference image path: magnet_insertion-proper.jpg
Input folder path: new_images
Python code: main.py
Code pdf: main.pdf
Output image folder: output images.zip
Project report: MOTOR ASSEMBLY MONITORING THROUGH IMAGE ANALYSIS.pdf
Presentation: MOTOR ASSEMBLY MONITORING THROUGH IMAGE ANALYSIS.pptx

## Slide 16: Relevance of the project to industrial applications.
The project "Motor Assembly Monitoring through Image Analysis" is highly relevant to industrial applications, particularly in the manufacturing sector. Here are some key aspects of its relevance:
Quality Assurance: By employing image analysis techniques to monitor motor assembly, manufacturers can ensure that each component is correctly positioned and fully inserted. This real-time monitoring reduces defects and improves overall product quality, essential for maintaining high standards in industrial applications.
Increased Efficiency: Automating the inspection process through image analysis significantly speeds up quality control compared to manual inspections. This efficiency allows for faster production cycles and the ability to identify and rectify issues immediately, minimizing downtime.
Cost Reduction: Detecting assembly issues early in the production process helps reduce costs associated with rework, waste, and product recalls. This project can lead to substantial savings for manufacturers by minimizing defects and improving yield rates.
Flexibility in Production: The ability to adapt image analysis techniques to various types of motor assemblies makes this approach versatile. Manufacturers can implement these methods across different product lines, enhancing flexibility and responsiveness to market demands.
Compliance and Safety: In industries where safety is critical, such as automotive or aerospace, ensuring the integrity of motor assemblies is paramount. Image analysis provides an objective assessment, helping companies comply with industry regulations and safety standards.
Reduced Human Error: Automated inspection reduces reliance on human judgment, which can be prone to error, fatigue, or oversight. This leads to more consistent and reliable quality assessments.

## Slide 17: Conclusion:
The program implements a comprehensive monitoring system for motor assembly through image analysis, focusing on magnet insertion quality. It begins by loading and preprocessing reference and test images, then compares them using the Structural Similarity Index (SSIM) and pixel-wise differences to evaluate assembly integrity. The system calculates various metrics, including surface roughness, magnet insertion percentage, and alignment scores, to assess the quality of assembly. Feature matching and depth analysis further enhance the understanding of discrepancies between the images. The decision-making module interprets these metrics against predefined thresholds to identify potential assembly issues, such as low SSIM values, incomplete magnet insertion, or high surface roughness. Finally, the program visualizes results and SSIM score distributions, enabling clear assessment of magnet insertion quality. This approach enhances quality control in manufacturing processes, ensuring that motor assemblies meet stringent standards for performance and reliability.
References:
Used tutorials: OpenCV, Matplotlib, scikit, python
YouTube- learned different thresholding techniques and Image Comparison Algorithms

## Slide 18
THANK YOU